## Slide 1
Security Challenges in Software Defined Networks (SDN)
Lecture 18

## Slide 2: Outline
Market and SDN
Conventional Networks v.s SDN
OpenFlow-enabled SDN devices
SDN Security Applications
SDN Security Challenges
Community Debate regarding Security in SDN

## Slide 3: Market and SDN
In 2016, the market research firm IDC predicted that the market for SDN network applications would reach US$3.5 billion by 2020.
Leading IT companies such as Nokia, Cisco, Dell, HP, Juniper, IBM, and VMware have developed their own SDN strategies.
In 2015, AT&T reduced provisioning cycle by 95% with SDN.
Marc C. Dacier, Hartmut Cwalinski , Frank Kargl , Sven Dietrich, Security Challenges and Opportunities of Software-Defined Networking, Apr 3, 2017
“We have taken a process from low automation and weeks to complete to high automation and minutes to complete. We’re turning the industry on its head in an unprecedented way.” John Donovan
AT&T’s analyst conference in August 2015, John Donovan
Notes: International Data Corporation (IDC), an American market research, analysis and advisory firm, specializes in information technology,
AT&T reduces provisioning cycle by 95% with SDN
reduction in the time spent ordering, managing and changing services by up up to 95%.
“We have taken a process from low automation and weeks to complete to high automation and minutes to complete. We’re turning the industry on its head in an unprecedented way.” John Donovan
John Donovan : senior executive vice president of technology and network operations

## Slide 4: Conventional Networks vs. SDN
  Customization
  Programmability
Control Plane
Data Plane
Dumb, fast
Control Plane
Data Plane
Abstract
view
  Global
  view
Control Plane
S
S
S
S
Network
Applications
Open
North-bound API
OpenFlow
South-bound API
  Traffic mngmnt,QoS
  Policy Imp.
  Security services
Decentralized Control
  Limited visibility
  Vendor-specfic
  Missconfiguration
  Poor responses
  Policy conflicts
  Security breaches
Decentralized.
Complex
Static architecture
Innovation is difficult
  Costly
  Yes costly
*Figure: Kreutz, Diego, et al. "Software-defined networking: A comprehensive survey." Proceedings of the IEEE 103.1 (2015): 14-76.
*
  Conventional Networks
Data Plane
  Software Defined Networks
Decoupling
Smart
Policy mngmnt

## Slide 5: OpenFlow-enabled SDN devices
Match Fields
*
00:2E
*
*
*
*
*
*
*
*
*
*
*
*
4.5.6.7
*
*
*
*
*
*
*
*
*
*
*
10
port3
port5
drop
Switching
Routing
Firewall
300
250
500
OpenFlow is: Enabler of SDN
  Protocol between the control plan and data plane
  Describes how controller and a network forwarding device should communicate
Packet+ byte Counters

## Slide 6: SDN security applications
Control Plane
Application plane
Routing, Load Balancer,
Access Control, monitoring, firewall, DDoS Mitigation, IDS/IPS
examples
Load Balancer: send each HTTP request over lightly loaded path to lightly loaded server.
Firewall: inform Central Controller about malware’s packets, controller pushes new rules to drop packets.
S
S
R
S
S
S
S
S
S
S
AB drop
Network Virtualization
Up-to-date Global Network View
Abstract Network View
Incoming packets
6
Server

## Slide 7: The big Picture SDN Archetucture
Alsmadi, Izzat, and Dianxiang Xu. "Security of software defined networks: A survey." Computers & security 53 (2015): 79-108.

## Slide 8
SDN Security Challenges

## Slide 9: Application Plane Security Challenges
  SDN aware & SDN unaware apps
  Nested applications
Lack of Access Control and Accountability
Lack of Authentication and Authorization
Fraudulent flow rule insertion
Path characteristics
Access ports
Monitor traffic
Reject/Accept flows
sensitive apps
Service apps
Apps classes

## Slide 10: Application Plane Targeted Threat/Proposed Solution
  Security policy
  verification framework
  -Flover:
  on controller
  new/old rules conflict
  -ndb: root cause
  -OFRewind : trace anomalies
  Security policy violation
Threats within/from apps
  flow rules contradiction
  Framework for security apps development
  (FRESCO Scripting language)
  Access control breach
  Assertion-based language
  -catch bugs before deployed
  - forwarding loops
  - black holes
  Permission system (PermOF ):
  least privilege on apps

## Slide 11: PermOF
Wen, Xitao, et al. "Towards a secure controller platform for openflow applications." Proceedings of the second ACM SIGCOMM workshop on Hot topics in software defined networking. ACM, 2013.
The design is based on a Set of permissions & Isolation mechanisms
  Ensures controller superiority over applications
  Isolates control flow and data flow
  controller should be able to mediate all the apps’ activity
Availability of sensitive info
real time
controlled by the controller kernel
dynamic
execute

## Slide 12
Control Plane Security Challenges
DoS Attacks
Threats due to Scalability
Challenges in Distributed Control Plane
  -SDN response times
  -IP packets with random headers
  -Huge # flow rules
  -saturation

## Slide 13
Control Plane Targeted Threat/Proposed Solution
  DDoS Attack
  Controller scalability
  Challenges in distributed control plane
  1. Wildcards mechanism
  -Load balancing: direct an aggregate of client requests to replicas
  2. Increase the processing power (McNettle controller) parallelism
  3. Hybrid reactively/Proactive controller
  Detection Framework
  SDN DDoSDetection
  intra-domain & inter-domain
  (DISO)
McNettle
http://haskell.cs.yale.edu/wp-content/uploads/2013/04/thesis-singlespace.pdf
NOX-MT scales to 5m f/s at 10 CPU cores
Beacon  13m f/s at 20 CPU cores
McNettle 20m f/s at 46 CPU cores

## Slide 14: Reactively vs. Proactive Controller
Marcial P. Fernandez, Evaluating OpenFlow Controller Paradigms, 2013

## Slide 15: SDN DDoSDetection
  Flow collector module: gathers flow entries within intervals.
  Feature extractor: Avg. packets/f, Avg. Bytes /f, avg duration/f, growth of single-flows, and growth of different ports.
  Classifier: Analyzes  Alarm?
R. Braga, E. Mota, and A. Passito, “Lightweight DDoS flooding attack detection using NOX/OpenFlow,” in Proc. IEEE 35th Conf. LCN, Oct. 2010, pp. 408–415.

## Slide 16: intra-domain & inter-domain (DISO)
  intra-domain : manages its own network domain
    compute the paths of flows
    dynamically react to network issues (broken line, high latency, bandwidth cap exceeded)
    redirecting and/or stopping traffic
  inter-domain:
    discovers neighboring controllers and manages communication among controllers
    exchange aggregated network-wide information with others
C2
C3
C1
SubD3
SubD2
SubD1
Traffic Optimization...
Topology!
Link information!
A

## Slide 17: Data Plane Security Challenges
Switch-Controller link
Flow rules installation
  Genuine vs. malicious rules
  Limited table entries
  Limited switch buffer
  #switches per controller
  path Length

## Slide 18: Data Plane Targeted Threat/Proposed Solution
  Real-time contradiction check
  FortNox
man-in-the-middle attacks
flow rule contradiction

## Slide 19
High level points
-- Debate

## Slide 20: Centralization in SDN
The Good:
Fast responsiveness
Easy to removing policy inconsistencies
  centralized routing algorithms
  Firewalls
  network-monitoring
  The Bad:
Single point of failure may be exploited by an internal or external attacker
Regarding DDoS
Bad: centralization added a new type of denial-of-service (DoS) vector.
Good: Effective management of existing DoS attack types
  Using Global view
  Traffic analysis
New security challenges but benefits appear to be predominant!!!
Marc C. Dacier, Hartmut Cwalinski , Frank Kargl , Sven Dietrich, Security Challenges and Opportunities of Software-Defined Networking, Apr 3, 2017

## Slide 21: Attack Surface vs. Defense Opportunities
Good:
In SDN defenders can create customized security solutions
e.g Anomaly detection systems
  Global view
  Open hardware interfaces
  Centralized control
Bad:
Benefit the attackers (zero day attacks)
  The centralized architecture
  Lack of defender expertise
  Still immature technology
Marc C. Dacier, Hartmut Cwalinski , Frank Kargl , Sven Dietrich, Security Challenges and Opportunities of Software-Defined Networking, Apr 3, 2017

## Slide 22: Centralized vs. Distributed Approach
Good:
Reduced complexity by splitting into planes.
  Easier testable
  E.g, routing algorithms simpler than the distributed approach in conventional networks.
Bad:
Stressed by two aspects that strongly call for the use of a distributed approach.
  The need for scalability
  Operational requirements (fault tolerance)
Marc C. Dacier, Hartmut Cwalinski , Frank Kargl , Sven Dietrich, Security Challenges and Opportunities of Software-Defined Networking, Apr 3, 2017

## Slide 23: Is SDN More Complex?, or Is It Simpler?
Implementing the control plane completely in software
Good :
Programmability
Bad:
Opposes simplicity : raises issues about algorithmic complexity.
  Why: additional requirements that weren’t imposed on classical networks but are now thinkable in SDN.
  Simplicity is a key design principle in building secure systems.
SDN has the potential to be simple—but making it simple is quite complex.
Marc C. Dacier, Hartmut Cwalinski , Frank Kargl , Sven Dietrich, Security Challenges and Opportunities of Software-Defined Networking, Apr 3, 2017

## Slide 24: Open problems & research directions
How to implement authentication and authorization to certify SDN applications.
How to implement access control and accountability in SDN.
How to implement customized security procedures based on the type or categories of applications.
How can we find automated derivation of Secure SDN Configurations.
How can we secure the controller-switches communication?
How can we perform efficient intrusion detection and anomaly detection in SDNs?
How can we operate SDN in presence of untrusted HW components?
How can we protect the controller itself?
Without security, SDN will not succeed!

## Slide 25
Thank you